## Slide 1: STOCHASTIC APPROACH To State Estimation Current Status and Open Problems
Jay H. Lee with help from Jang Hong and Suhang Choi
Korea Advanced Institute of Science and Technology
Daejeon, Korea
FIPSE -1
Olympian Village
Western Peloponnese, GREECE
29-31, August 2012

## Slide 2: Some Questions Posed for This Session
Is state estimation a mature technology?
Deterministic vs. stochastic approaches – fundamentally different?
Modeling for state estimation – what are the requirements and difficulties?
Choice of state estimation algorithm – Tradeoff between performance gain vs. complexity increase: Clear?
Emerging applications – posing some new challenges in state estimation?

## Slide 3: Part I
Introduction

## Slide 4: The Need of State Estimation
State Estimation is an integral component of
  Process Monitoring: Not all variables of importance can be measured with enough accuracy.
  RTO and Control: Models contain unknowns (unmeasured disturbances, uncertain parameters, other errors)
State estimation enables the combining of system information (model) and on-line measurement information for
  Estimation of unmeasured variables / parameters
  Filtering of noises
  Prediction of system-wide future behavior

## Slide 5: Deterministic vs. Stochastic Approaches
Deterministic Approaches
  Observer approach, e.g., pole placement, asymptotic obs.
  Optimization-based approach, e.g., MHE
  Focus on state reconstruction w/ unknown initial state
  Emphasis on the asymptotic behavior, e.g., observer stability
  There can be many “tuning” parameters (e.g., pole locations, weight parameters) difficult to choose.
Stochastic Approaches
  Require probabilistic description of the unknowns (e.g., initial state, state / measurement noises)
  Observer approach: Computation of the parameterizd gain matrix minimizing the error variance, or
  Bayesian Approach: Recursive calculation of the conditional probability distribution

## Slide 6: Deterministic vs. Stochastic Approaches
Stochastic approaches require (or allow for the use of) more system information but can be more efficient and also return more information (e.g., uncertainty in the estimates, etc.)
  Important for “information-poor” cases
Both approaches can demand selection of “many” parameters difficult to choose, e.g., the selection of weight parameters amounts to the selection of covariance parameters.
Stochastic analysis reveals fundamental limitations of certain deterministic approaches, e.g., Least squares minimization leading to a linear type estimator is optimal for the Gaussian case only.
In these senses, stochastic approaches are perhaps more general but deterministic observers may provide simpler solution for certain problems (“info-rich” nonlinear problems).

## Slide 7: Is State Estimation A Technology?
For state estimation to be a mature technology, the followings must be routine:
  Construction of a model for state estimation – including the noise model
  Choice of estimation algorithms
  Analysis of the performance limit
Currently,
  The above are routine for linear, stationary, Gaussian type process.
  Far from being routine for nonlinear, non-stationary, non-Gaussian cases (most industrial cases)!

## Slide 8: Part II
Modeling for State Estimation

## Slide 9: Modeling Effort vs. Available Measurement
Sensed Information
Quantity (Number)
Quality (Accuracy, Noise)
Model
Model of the Unknowns (Disturbance / Noise)
Model Accuracy
“Information-rich” case: No need for a detailed (structured) disturbance model. In fact, an
effort to introduce such a model can result in a robustness problem.
“Information-poor” case: Demands a detailed (structured) disturbance model for good
performance.
Complementary!

## Slide 10: Illustrative Example

## Slide 11: Simulation results
Full information cases
For the “info-rich” case, model error from detailed dist. modeling can be damaging.
For 1th element of x
For 10th element of x
For 21th element of x
RMSE | 0.0124 | 0.0081 | 0.1032
RMSE: Root Mean Square Error

## Slide 12: Illustrative Example

## Slide 13: Simulation results
Information-poor case
For the “info-poor” case, detailed disturbance modeling is critical!
For 1th element of x
For 10th element of x
For 21th element of x
RMSE | 0.4107 | 0.0759 | 0.2484
RMSE: Root Mean Square Error

## Slide 14: Characteristics of Industrial Process Control Problems
Relatively large number of state variables compared to number of measured variables
Noisy, inaccurate measurements
Relatively fewer number of (major) disturbance variables compared to number of state variables
Many disturbance variables have integrating or other persistent characteristics ⇒ extra stochastic states needed in the model
Typically, “info-poor”, structured unknown case
Demands detailed modeling of disturbance variables!

## Slide 15: Construction of a Linear Stochastic System Model for State Estimation
Linear System Model for Kalman Filtering:
{A, B, C, K, Cov(e)}
within some similarity transformation
Innovation Form:
Data-Driven, e.g.,
Subspace ID
Disturbance:
Measurement Noise:
Deterministic Part:
Knowledge-Driven
These procedures often result in increased state dimension and R1 and R2 that are very ill-conditioned!

## Slide 16: A Major Concern: Non-Stationary Nature of Most Industrial Processes
Time-varying characteristics
  S/N ratio: R1/R2 change with time.
  Correlation structure: R1 and R2 change with time
  Disturbance characteristics: The overall state dimension and system matrices can change with time too.
“Efficient” state estimators that use highly structured noise models (e.g., ill-conditioned covariance matrices) are often not robust!
  Main reason for industries not adopting the KF or other state estimation techniques for MPC.

## Slide 17: Potential Solution 1: On-Line Estimation of R1 and R2 (or the Filter Gain)
Autocovariance Least Squares (ALS), Rawlings and coworkers, 2006.

## Slide 18: ALS Formulation
Model with IWN disturbance
Case II: Updated disturbance covariance
Case I: Fixed disturbance covariance

## Slide 19: ALS Formulation
Linear least squares estimation (Case I) or nonlinear least squares Estimation (Case II)
Positive semi-definiteness constraint ⇒Semi-definite programming
Takes a large number of data points for the estimates to converge
  Not well-suited for quickly / frequently changing disturbance patterns.
Estimate of Auto-covariance matrix from the data
Innovation data

## Slide 20: Illustrative Example of ALS
From Odelson et al., IEEE Control System Technology, 2006

## Slide 21: ALS vs. without ALS
Servo Control with Model Mismatch
Input Disturbance Rejection

## Slide 22: Potential Solution #2: Multi-Scenario Model w/ the HMM or MJLS Framework
1
2
(A1, B1, C1, Q1, R1)
(A2, B2, C2, Q2, R2)
Wong and Lee, Journal of Process Control 2010

## Slide 23: Markov Jump Linear System Restricted Case

## Slide 24: Illustrative Example: input/ output disturbance models
i/ p disturbance
o/ p disturbance
HMM Disturbance Model for Offset-free LMPC

## Slide 25: Disadvantages
Either input or output disturbance
Plant-model mismatch
{Gd = 0, Gp = Iny}
  sluggish behavior
  might add state noise to compensate
IWN disturbance models are too simplistic
  do not always capture dynamic patterns seen in practice
HMM Disturbance Model for Offset-free LMPC

## Slide 26: Potential disturbance scenario probabilistic transitions b/w regimes
HMM Disturbance Model for Offset-free LMPC
A hypothesized disturbance pattern common in process industries

## Slide 27: Probabilistic transitions Markov chain modeling
LO-LO
(r = 1)
HI-LO
(r = 3)
HI-HI
(r = 4)
A 4-state Markov Chain
LO-HI
(r = 2)
HMM Disturbance Model for Offset-free LMPC

## Slide 28: Plant model –(1) Markov Jump Linear System
HMM Disturbance Model for Offset-free LMPC

## Slide 29: Plant model –(2) Markov Jump Linear System
HMM Disturbance Model for Offset-free LMPC

## Slide 30: Detectable formulation* after differencing
* used by estimator/ controller
HMM Disturbance Model for Offset-free LMPC

## Slide 31: Example
(A = 0.9, B = 1, C = 1.5)
Unconstrained optimization
HMM Disturbance Model for Offset-free LMPC

## Slide 32: Simulations 4 scenarios*
1: Input noise << output noise (LO-HI)
2: Input noise >> output noise (HI-LO)
3: Input noise ~ output noise (HI-HI)
4: Switching disturbances
*: use parameters given in previous table
HMM Disturbance Model for Offset-free LMPC

## Slide 33: Four estimator/ controller designs
1. Output disturbance only
  Kalman filter
2. Input disturbance only
  Kalman filter
3. Output and input disturbance
  Kalman filter
4. Switching behavior
  need sub-optimal state estimator
HMM Disturbance Model for Offset-free LMPC

## Slide 34: Mean of relative squared error (500 realizations*)
HMM Disturbance Model for Offset-free LMPC
*: normalized over benchmarking controller (known Markov state)

## Slide 35: Scenario 4 switching disturbance – y vs. time

## Slide 36: Construction of A Nonlinear Stochastic System Model for State Estimation
Linear System Model for Kalman Filtering:
{f,g}
Nonlinear Subspace Identification?
Innovation Form:
Data-Driven
Disturbance:
Measurement Noise:
Deterministic Part:
Knowledge-Driven
Data-Based Construction of A Nonlinear Stochastic System Model Is An Important Open Problem!

## Slide 37: Part III
State Estimation Algorithm

## Slide 38: State of The Art
Linear system (w/ symmetric (Gaussian) noise)
  Kalman Filter – well understood!
Mildly nonlinear system (w/ reasonably well-known initial condition and small disturbances)
  Extended Kalman Filter (requiring Jacobian calculation)
  Unscented Kalman Filter (“derivative-free” calculation)
  Ensemble Kalman Filter (MC sample based calculation)
(Mildly) Linear system (w/ asymmetric (non-Gaussian) noise)?
  KF is only the best linear estimator. Optimal estimator?
Strongly nonlinear system?
  Resulting in highly non-gaussian (e.g., multi-modal) distributions
  Recursive calculations of the first two moments do not work!

## Slide 39: EKF - Assessment
The extended Kalman filter is probably the most widely used estimation algorithm for nonlinear systems.
However, more than 35 years of experience in the estimation community has shown that it is difficult to implement, difficult to tune, and only reliable for systems that are almost linear on the time scale of the updates.
Many of these difficulties arise from its use of linearization
Julier and Uhlmann (2004)

## Slide 40: Illustrative Example
Rawlings and Lima (2008)
P

## Slide 41: Steady-State Error Results – Despite Perfect Model Assumed.
Concentration
Pressure
Time
Time
A
A
B
B
C
C
Component | Predicted EKF Steady-State | Actual Steady-State
A | -0.027 | 0.012
B | -0.246 | 0.183
C | 1.127 | 0.666
Real
Estimates

## Slide 42: EKF vs. UKF
2L+1
(⇒UKF)
Similar calculations are performed for the measurement update step.

## Slide 43: EKF vs. UKF
 | EKF | UKF
What’s tracked | First two moments | First two moments
Procedure | Linearization | Approximation w/ 2L+1 sigma points
Computation | Single integration at each step Requires calculation of the Jacobian matrices | Up to 2L+1 integrations at each step “Derivative-free”
The Verdict | Extensively tested Works well for mildly linear systems with good initial guess Can show divergence otherwise | Developed and tested mostly for aerospace navigation and tracking problems Often shows improved performance over the EKF

## Slide 44: EKF vs. UKF: Illustrative Examples
Romanenko and Castro, 2004
  4 state non-isothermal CSTR
  State nonlinearity
  The UKF performed significantly better than the EKF when the measurement noises were significant (requiring better prior estimates)
Romanenko, Santos, and Afonso, 2004
  3 state pH system
  Linear state equation, highly nonlinear output equation.
  The UKF performed only slightly better than the EKF
In what cases does the UKF fail? Computational complexity between EKF vs. UKF?

## Slide 45: BATCH (Non-Recursive) Estimation: Joint-MAP Estimate
Probabilistic Interpretation of the Full-Information Least Squares Estimate (Joint MAP Estimate)
Nonlinear, nonconvex program in general.
Constraints can be added.
(By taking negative logarithm)
System

## Slide 46: Recursive: Moving Horizon Estimation
Initial Error Term – Its Probabilistic Interpretation
Negative effect of linearization or other approximation declines with the horizon size

## Slide 47: MHE for Nonlinear Systems: Illustrative Examples
Concentration
Time
A
A
B
B
C
C
Pressure
Time
Component | Predicted MHE Steady-State | Actual Steady-State
A | 0.012 | 0.012
B | 0.183 | 0.183
C | 0.666 | 0.666
Real
Estimates

## Slide 48: MHE for Strongly Nonlinear Systems: Illustrative Examples
RMSE = 21.2674
RMSE = 13.3920
States
Estimates
EKF
MHE

## Slide 49: MHE for Strongly Nonlinear Systems: Shortcomings and Challenges
RMSE is improved, but still high ~ Multi-modal density
Nonlinear MHE requires ~ 1) Non-convex optimization method 2) Arrival cost approximation
Mode 1
Mode 2
MHE approximate the arrival cost based on (uni-modal) normal distribution → Hard to handle the multi-modal density that can arise in a nonlinear system within MHE

## Slide 50: MHE for Strongly Nonlinear Systems: Shortcomings and Challenges
The exact calculation of the initial state density function is generally not possible.
  Approximation is required for the initial error penalty.
  Estimation quality depends on the choice of approximation and the horizon length.
  How to choose the approximation and the horizon length appropriately.
Solving the NLP on-line is computationally demanding
  How to guarantee a (suboptimal) solution within a given time limit, while guaranteeing certain properties?
How to estimate uncertainty in the estimate?

## Slide 51: MLE with Non-Gaussian Noises as Constrained QP
Maximum Likelihood Estimation
Robertson and Lee, Automatica, 2002 “On the Use of Constraints in Least Squares Estimation”
Asymmetric distribution

## Slide 52: MLE with Non-Gaussian Noises as Constrained QP
Other common types of nonGaussian density for which MLE is expressed as QP.
Joint MAP estimation of the state for a linear system with such non-Gaussian noise terms can be formulated as a QP. ⇒ Optimal handling of some non-Gaussian noises is possible within MHE?

## Slide 53: Particle Filtering for Strongly Nonlinear Systems
Sampled
densities
Sampled
densities

## Slide 54: PF: Degeneracy Problem
Degeneracy phenomenon after a few iterations
Increasing variance of weights

## Slide 55: PF: Optimal Importance Density
System
Covaricance
Mean
~ Nonlinear dynamics
~ Linear measurements
Importance
density

## Slide 56: Particle Filtering for Strongly Nonlinear Systems: Illustrative Examples
RMSE (mean) = 7.1452
RMSE (mode) = 9.5829
RMSE (mean) = 4.7477
RMSE (mode) = 5.9934
PF
PF with optimal importance function
States
Estimates (mean)
Estimates (mode)
~ Nonlinear
~ Linear

## Slide 57: PF: Resampling
Optimal importance function calculation is not possible in general.
Resampling → Removing small weights and equalizing weights
② Assign sample ~ Uniform distribution

## Slide 58: Particle Filtering for Strongly Nonlinear Systems: Illustrative Examples
RMSE (mean) = 9.6864
RMSE (mode) = 9.5829
RMSE (mean) = 4.9992
RMSE (mode) = 6.7416
M. S. Arulampalam et al., IEEE Transactions on Signal Processing, 50, 2 (2002) (Number of particles: 1000)
PF without resampling
PF with resampling
States
Estimates (mean)
Estimates (mode)

## Slide 59: Particle Filtering for Strongly Nonlinear Systems: Illustrative Example
Sampled density function propagation in particle filtering
The state estimation is proceeded based on multimodal distribution

## Slide 60: Particle Filtering for Strongly Nonlinear Systems: Shortcomings and Challenges
Optimal importance function ~ hard to choose in general but…
Resampling ~ degeneracy vs. diversity
Number of particles ~ accuracy vs. computational time
Difficult to apply to high-dimensional systems
  Hybrid between nonparametric and parametric approach?
Chart: 
| 100 | 200 | 500 | 1000
 | 5.6053 | 5.2435 | 5.0097 | 4.9454
Chart: 
| 100 | 200 | 500 | 1000
 | 0.41687 | 0.74877 | 1.7613 | 3.4388
RMSE
Computational time
Number of particles
Number of particles

## Slide 61: Particle Filtering for Strongly Nonlinear Systems: Shortcomings and Challenges
Fundamentally hard to handle high-dimensional model within PF. ~ Very large ensemble is required to avoid collapse of weights.
(C. Snyder et al., Mathematical Advances in Data Assimilation, 136 (2008))
Required ensemble size Ne as a function of Nx (= Ny)
Even for a simple example
→ Exponentially increasing!
Notes: Average squared error of the posterior less than the prior or observations

## Slide 62: Integration of State Estimation and Control
State estimation giving fuller information (more than a point estimate):
  How do we design controllers utilizing the extra information like uncertainty estimates, multiple point estimates, or even the entire distribution?
  How do we design the state estimator and controller in an integrated manner when the separation principle breaks down?

## Slide 63: Part IV
Emerging Application

## Slide 64: Nano-Sensor Arrays
Atomic force microscopy (AFM) image of
AT15-SWNT
Front and side schematic views of AT15-SWNT
Near-infrared fluorescence image of AT15-SWNT
Carbon nanotube-based sensor arrays on 2D field
Light
emission

## Slide 65: Applications of Nano-Sensor Arrays
Tissue engineering ~ Signaling drug delivery
Manufacturing ~ Nano products
Monitoring ~ Environment sensing
Stem cells
Scaffold
Signaling molecules
Organ
Sensor arrays

## Slide 66: Local Sensor: Parameter Estimation
DNA
CNT
Target molecule
Adsorption site
Continuum equation
Chemical master equation
Vs.

## Slide 67: Local Sensor: Some Results
Maximum likelihood estimation with data from a single CNT sensor (Zachary W. Ulissi et al., J. Physical Chemistry Letters, 2010)
Not real-time estimation & not considering spatial and temporal concentration variations → Sensor arrays should be considered
→ Convolution of Binomial distribution
Traces
 | 10 traces | 100 traces | 1000 traces | 10000 traces

## Slide 68: Nano-Sensor Arrays: New Challenges in State Estimation
2D sensor array in micro-scale ~ A very high-dimensional system
DNA
CNT
1D Diffusion Eq.

## Slide 69: Challenges
A very large number of sensors placed on a distribu-ted parameter system
  A very high dimensional problem
Complex probabilistic measurement equation
  Not the usual
  Chemical master equation
Diffusion equation, etc.
  Structure in the system equation (e.g., symmetry, sparseness)
  How to take advantage of it?

## Slide 70: Fast Moving Horizon Estimation
Assume the local concentration can be estimated reliably from each CNT sensor.
Singular value decomposition of the system matrix for decoupling
Constraint handling: Linear constraints couple the decoupled system!
  Ellipsoid constraint approximation
  Penalty method

## Slide 71: Fast MHE: Some Results
Chart: log State dimension
| 11 | 21 | 51 | 101
QP | 0.185 | 0.238 | 0.531 | 1.311
SVD based QP | 0.0167 | 0.0189 | 0.0196 | 0.02
 | 0.12873 | 0.27525 | 0.78096 | 1.7434 | 0
 | 0.017263 | 0.018125 | 0.01938 | 0.020405
Original MHE
Proposed MHE
Computational time
~1.175
~ 0.075
Average error
Chart: State dimension
| 11 | 21 | 51 | 101
QP | 0.0146 | 0.0132 | 0.0109 | 0.0093
element-wise QP | 0.016 | 0.0147 | 0.0121 | 0.0106

## Slide 72: Image / Spectroscopy Sensors
Video cameras
  RGB images
Spectroscopy
  Light scattering, absorption, emission, coherence, resonance, etc.
These types of sensors
  Noisy, high dimensional data with complex multivariate relationships to physical variables of interest
  often require significant signal processing (calibration, image processing)

## Slide 73: Illustrative Example: Food Processing
MacGregor and coworkers CIL (2003), I&ECR (2003)
Multivariate Image Analysis

## Slide 74: Image / Spectroscopy Sensors: New Challenges in State Estimation
State Space
Model
Image
Processing:
PCA
PLS
Wavelet
Estimates
of physical variables yk
Often complex and can be probabilistic!
Two step or one step?
Noisy
Images
Can be complex!

## Slide 75: Conclusion: Some Questions Posed for This Session
Is state estimation a mature technology?
  For linear Gaussian stationary systems, yes. Otherwise no. May never be!
Deterministic vs. stochastic approaches – fundamentally different?
  Stochastic approach is perhaps more general and provides more information but deterministic observer may provide simpler solutions for certain problems (e.g., “info-rich” nonlinear problems.
  Stochastic interpretation of certain deterministic approaches
Modeling for state estimation – what are the requirements and difficulties?
  Disturbance modeling: Right level of detail depends on the amount of measurement information available.
  Data-based modeling for linear stationary systems: Subspace ID.
  Some partial solutions for linear non-stationary systems.
  Data-based modeling for nonlinear systems: an open question!

## Slide 76: Conclusion: Some Questions Posed for This Session
Choice of state estimation algorithm – performance gain vs. complexity increase: Clear?
  KF EKFUKFMHEPF: Right choice is not always clear.
  Tools are needed for this.
Emerging applications – posing some new challenges in state estimation.
  New types of sensors, e.g., nano sensor arrays, image or spectroscopic sensors
  Complex probabilistic measurement equation, e.g., chemical master equation

## Slide 77: Interesting Open Challenges!
“Information-Poor” Case
  High dimensional state space
  Structured errors (ill-conditioned state covariance matrices)
  Nonlinear, non-Gaussian…
Complex Stochastic Measurement Case
  Physical state / output variables affect the probability distribution in the stochastic measurement process
  Perhaps large number of distributed sensors on a distributed parameter system.

## Slide 78: Acknowledgment
Graduate Students at KAIST
  Jang Hong, Ph.D. student
  Suhang Choi, M.S. student
Prof. Richard Braatz (MIT)
Financial Support
  Global Frontier Advanced Biomass Center